## Slide 1
SDC-ToBe
Swarm Drone Challenge 2026
Technical Architecture & Stack Overview
Multi-drone swarm control platform with real-time ArUco positioning, autonomous navigation, and competitive game strategy

## Slide 2
System Architecture
C2 Strategy Dashboard
Game AI, phase management, scoring FastAPI + WebSocket (port 9090)
C2 Interface
Web UI, grid map, mission control FastAPI + WebSocket (port 8080)
Unified API Server
REST API, RC control, video, telemetry Flask on Raspberry Pi (port 8080)
Drone Hardware / Simulator
DJI Tello | Parrot Anafi | Sim WiFi 2.4GHz, Olympe/djitellopy SDK
ArUco Positioning
▸ 25 wall-mounted markers
▸ OpenCV ArUco detection
▸ solvePnP pose estimation
▸ Kalman filter smoothing
▸ 20m x 10m arena grid
▸ Markers at 2m + 4m height
▸ 18x18 cm marker size
▸ SSE + UDP position relay
WiFi 2.4GHz | HTTP REST | WebSocket | SSE | UDP

## Slide 3
Tech Stack
Backend
▸ Python 3.11+
▸ FastAPI + Uvicorn (C2)
▸ Flask (Pi controllers)
▸ Pydantic data models
▸ Threading / async-await
Vision & Sensing
▸ OpenCV 4.13 (ArUco)
▸ Camera calibration (NPZ)
▸ solvePnP 3D localization
▸ Kalman filter (1D/3D)
▸ Power-law distance calib.
Drone SDKs
▸ djitellopy 2.5 (Tello)
▸ Parrot Olympe (Anafi)
▸ Auto-detect by IP addr
▸ ARM-safe conditional import
▸ Gimbal + GPS (Anafi)
Frontend & Comms
▸ Vanilla JS + CSS Grid
▸ WebSocket (real-time)
▸ SSE telemetry streams
▸ MJPEG video streaming
▸ UDP position relay

## Slide 4
Supported Drones
DJI Tello
▸ SDK: djitellopy 2.5
▸ Control: UDP socket
▸ Default IP: 192.168.10.1
▸ Video: 960x720 MJPEG
▸ Telemetry: battery, height, IMU
▸ Multi-drone: per-WiFi-stick isolation
Parrot Anafi
▸ SDK: Parrot Olympe (x86 only)
▸ Control: Olympe PCMD + moveBy
▸ Default IP: 192.168.42.1
▸ Video: 1280x720 (up to 4K)
▸ Sensors: GPS, gimbal, barometer
▸ Features: RTH, geofence, flight config
Simulator
▸ 4 variants (2D, 3D, API, C2)
▸ Drop-in API replacement
▸ Physics: velocity model
▸ 3D web viewer (Three.js)
▸ Configurable arena & targets
▸ No hardware required

## Slide 5
Unified API Server
Single REST endpoint auto-detects drone type (Tello vs Anafi) by IP address
Endpoint | Method | Description
/api/takeoff | POST | Take off
/api/land | POST | Land
/api/rc | POST | Raw RC control (lr, fb, ud, yaw: -100..100)
/api/move | POST | Discrete move (direction + cm)
/api/telemetry | GET | Full telemetry snapshot (JSON)
/api/telemetry/stream | GET | SSE telemetry stream (~2.5 Hz)
/api/video/start | POST | Start MJPEG video stream
/api/video | GET | MJPEG stream output
/api/position | GET | Current ArUco position
/api/position/events | GET | SSE position updates
/api/position/video | GET | MJPEG with ArUco overlay
/api/settings | GET/POST | Flight limits (persisted to JSON)
/api/heartbeat | GET | Watchdog keepalive

## Slide 6
ArUco Positioning System
1. Detection
OpenCV detects ArUco 4x4 markers in each video frame
2. Pose Estimation
solvePnP computes 3D camera position from marker corners
3. Kalman Filter
Smooths noisy measurements for stable positioning
4. Relay
SSE + UDP streams position to C2 at ~2.5 Hz
Arena Configuration
▸ 20m wide x 10m deep arena
▸ 25 markers (ID 0-24) on 4 walls
▸ Front, Back, Left, Right walls
▸ Each marker at 2m or 4m height
▸ Physical marker size: 18x18 cm
▸ ArUco dictionary: 4x4_100
Distance Calibration
▸ Power-law: dist = 109.17 * px^(-0.897)
▸ Empirical fit from measured data
▸ 55px = 3.0m, 85px = 2.0m, 180px = 1.0m
▸ Camera intrinsics via calibration.npz
▸ Client-side ArUco (VideoMarkerTracker)
▸ Perspective skew for angle detection

## Slide 7
Autonomous Tool: ArUco Seek & Approach
TAKEOFF
Climb to target altitude
SETTLE
Stabilize (3 seconds)
SCAN
Rotate 360° find markers
ALIGN
Yaw to face marker dead-on
APPROACH
Fly forward to target dist
HOVER
Hold position 1.5m from marker
Visual Servoing
▸ Pure image-based control (no world coordinates)
▸ Marker center in image -> yaw + altitude correction
▸ Pixel size -> distance estimate (calibration curve)
▸ Perspective skew -> lateral strafe correction
▸ Edge-boost: 3x gain when marker nears frame edge
▸ P-controllers: yaw P=40, alt P=45, dist P=8
▸ Works with ANY room setup (no arena config needed)
Safety & CLI
▸ Ctrl+C: abort and land immediately
▸ Watchdog heartbeat every 400ms
▸ Auto-land on 120s timeout
▸ Auto-land if marker lost for 8s
▸ --marker <ID>: target specific marker
▸ --hover-distance: set standoff distance
▸ --record: save debug video (MJPEG)

## Slide 8
Command & Control Interfaces
C2 Interface (Team Control)
▸ FastAPI + WebSocket (port 8080)
▸ 20m x 10m arena grid (200 cells)
▸ Zone system: Red | Neutral | Blue
▸ Click-to-navigate: select drone, click cell
▸ Per-drone MJPEG video panels
▸ Mission flow: navigate -> search -> hover -> return
▸ Modes: live (real drones), simulator, sim_api
▸ Multi-WiFi isolation for 2-5 real Tellos
▸ Target designation (up to 6 per team)
C2 Strategy (Game AI)
▸ FastAPI + WebSocket (port 9090)
▸ Rule-based strategy engine
▸ Game phases:
▸ SETUP -> SCOUTING -> ATTACK
▸ -> TEAM_RETURN -> DEFEND
▸ -> INSTANT_WIN -> GAME_OVER
▸ Drone roles: Scout, Attacker,
▸ Defender, Returner
▸ Live ArUco position via UDP relay
▸ Scoring logic + win detection

## Slide 9
Simulation Environments
2D Swarm Sim
sim_swarm/
▸ Lightweight (no ext. deps)
▸ Scenario-based testing
▸ baseline, degraded_link, dropout
▸ Metrics: time, collisions, battery
▸ Timeline replay in web viewer
3D API Simulator
sim_swarm_API/
▸ Full HTTP + WebSocket API
▸ Three.js 3D web visualization
▸ Drop-in for unified API
▸ Swarm mission logic
▸ ArUco marker simulation
HTTP/UDP Drone Sim
drone-sim/
▸ Minimal physics model
▸ Tello-compatible HTTP API
▸ UDP JSON telemetry output
▸ Single-file (14KB)
▸ Configurable targets
C2-Integrated Sim
sim_swarm_c2/
▸ Full game simulation
▸ Strategy engine overlay
▸ Multi-drone coordination
▸ Phase + role testing
▸ Scoring validation

## Slide 10
Communication & Data Flow
Channel | Protocol | Frequency | Direction | Purpose
Drone Control | HTTP REST | On-demand | C2 -> Pi -> Drone | Takeoff, land, move, RC
Telemetry | SSE (HTTP) | ~2.5 Hz | Drone -> Pi -> C2 | Battery, height, yaw, status
Video Feed | MJPEG (HTTP) | 15-30 FPS | Drone -> Pi -> Client | Live camera stream
ArUco Position | SSE + UDP | ~2.5 Hz | Pi -> C2 / Tools | x, y, z, velocity, markers
C2 Dashboard | WebSocket | Real-time | Bidirectional | State updates, commands
RC Commands | HTTP POST | 5 Hz | Tool -> Pi | lr, fb, ud, yaw (-100..100)
Heartbeat | HTTP GET | 2.5 Hz | Tool -> Pi | Watchdog keepalive
Video Record | Server-side | Frame rate | Pi local | MP4 with ArUco overlay

## Slide 11
By the Numbers
~67
Python Modules
10
Major Systems
3
Drone Types
4
Simulator Variants
25
ArUco Markers
40+
REST API Endpoints
200
Arena Grid Cells (1m²)
18cm
Marker Size

## Slide 12
Project Structure
Directory | Purpose | Key Tech
controller_unified/ | Unified Pi API server (Tello + Anafi) | Flask, OpenCV, Olympe
c2_interface/ | Web-based team C2 (grid map, missions) | FastAPI, WebSocket, JS
c2_strategy/ | Strategic game AI + scoring | FastAPI, state machine
aruco-position/ | ArUco detection + 3D localization | OpenCV, solvePnP, Kalman
tools/ | Autonomous drone tools (aruco_seek) | Visual servoing, P-control
sim_swarm/ | Lightweight 2D swarm simulation | Pure Python, scenarios
sim_swarm_API/ | Full 3D simulator + web viewer | FastAPI, Three.js
drone-sim/ | Minimal HTTP/UDP drone simulator | Flask, physics model
sim_swarm_c2/ | C2-integrated game simulation | Strategy + sim combined
1_Doc/ | Documentation, specs, calibration | PDF, DOCX, XLSX